## Slide 1: Routing 2014
Geoff Huston
APNIC

## Slide 2: Looking through the Routing Lens

## Slide 3: Looking through the Routing Lens
There are very few ways to assemble a single view of the entire Internet
The lens of routing is one of the ways in which information relating to the entire reachable Internet is bought together
Even so, its not a perfect lens…

## Slide 4: There is no Routing God!
There is no single objective “out of the system” view of the Internet’s Routing environment.
BGP distributes a routing view that is modified as it is distributed, so every eBGP speaker will see a slightly different set of prefixes, and each view is relative to a given location
So the picture I will be painting here is one that is drawn from the perspective of AS131072. This is a stub AS at the edge of the Internet.
You may or may not have a similar view from your network.

## Slide 5
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Broadband to the Masses
2009: The GFC hits the Internet
2011: Address Exhaustion
20 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route Views

## Slide 6
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Broadband to the Masses
2009: The GFC hits the Internet
2011: Address Exhaustion
20 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route Views

## Slide 7: 2014, as seen at Route Views

## Slide 8: 2014, as seen at Route Views
The last quarter of 2014 saw routing system growth drop off

## Slide 9: Routing Indicators for IPv4
Routing prefixes – growing by some 45,000 prefixes per year
AS Numbers– growing by some 3,000 prefixes per year

## Slide 10: Routing Indicators for IPv4
More Specifics are still taking up one half of the routing table
But the average size of a routing advertisement is getting smaller

## Slide 11: Routing Indicators for IPv4
Address Exhaustion is now visible in the extent of advertised address space
The “shape” of inter-AS interconnection appears to be steady, as the Average AS Path length has been held steady through the year

## Slide 12: What happened in 2014 in V4?
From the look of the growth plots, its business as usual, despite the increasing pressure on IPv4 address availability
You may have noticed that the number of IPv4 routes cross across the threshold value of 512,000 routes in the last quarter of 2014
  And for some routers this would’ve caused a hiccup or two
You can also see that the pace of growth of the routing table is dropping off towards the end of the year
  IPv4 address exhaustion is probably to blame here!

## Slide 13: How can the IPv4 network continue to grow when we are running out of IPv4 addresses?
We are now recycling old addresses back into the routing system
Some of these addresses are transferred in ways that are recorded in the registry system, while others are being “leased” without any clear registration entry that describes the lessee

## Slide 14: IPv4 Address Reuse

## Slide 15: IPv4 Address Reuse
50% of new addresses in 2014 were more than 1 year old
20% of new addresses in 2010 were more than 1 year old
18% of new addresses in 2014 were more than 20 years old
It appears that this collection of “old” addresses includes space that has been leased rather than transferred

## Slide 16: IPv4 in 2014 – Growth is Slowing
Overall IPv4 Internet growth in terms of BGP is at a rate of some ~9%-10% p.a.
Address span growing far more slowly than the table size (although the LACNIC runout in May ’14 caused a visible blip in the address consumption rate)
The rate of growth of the IPv4 Internet is slowing down, due to:
  Address shortages
  Masking by NAT deployments
  Saturation of critical market sectors
  Transition uncertainty

## Slide 17: The Route Views view of IPv6
World IPv6 Day
IANA IPv4 Exhaustion

## Slide 18: 2014 for IPv6, as seen at Route Views

## Slide 19: Routing Indicators for IPv6
Routing prefixes – growing by some 6,000 prefixes per year
AS Numbers– growing by some 1,600 prefixes per year (which is half the V4 growth)

## Slide 20: Routing Indicators for IPv6
More Specifics now take up one third of the routing table
The average size of a routing advertisement is getting smaller

## Slide 21: Routing Indicators for IPv6
Address consumption is happening at a constant rate, and not growing year by year
The “shape” of inter-AS interconnection appears to be steady, as the Average AS Path length has been held steady through the year

## Slide 22: IPv6 in 2014
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2012 growth rate was ~ 90%.
If these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in ~16 years time

## Slide 23: What to expect

## Slide 24: BGP Size Projections
For the Internet this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
    Uncertainty over IPv6 takeup leads to a mixed response to IPv6 so far, and no clear indicator of trigger points for change
  all of which which make this year’s projection even more speculative than normal!

## Slide 25: V4 - Daily Growth Rates

## Slide 26: V4 - Daily Growth Rates

## Slide 27: V4 - Relative Daily Growth Rates

## Slide 28: V4 - Relative Daily Growth Rates
Growth in the V4 network appears to be constant at a long term average of 120 additional routes per day, or some 45,000 additional routes per year
Given that the V4 address supply has run out this implies further reductions in address size in routes, which in turn implies ever greater reliance on NATs
Its hard to see how and why this situation will persist at its current levels over the coming 5 year horizon

## Slide 29: IPv4 BGP Table Size predictions
Jan 2013 441,000 entries
2014 488,000
2015 530,000
2016 580,000
2017 620,000
2018 670,000
2019 710,000
2020 760,000
These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.

## Slide 30: IPv6 Table Size

## Slide 31: V6 - Daily Growth Rates

## Slide 32: V6 - Daily Growth Rates

## Slide 33: V6 - Relative Growth Rates

## Slide 34: V6 - Relative Growth Rates
Growth in the V6 network appears to be increasing, but in relative terms this is slowing down.
Early adopters, who have tended to be the V4 transit providers, have already received IPv6 allocation and are routing them. The trailing edge of IPv6 adoption are generally composed of stub edge networks in IPv4. These networks appear not to have made any visible moves in IPv6 as yet.
If we see a change in this picture the growth trend will likely be exponential. But its not clear when such a tipping point will occur

## Slide 35: IPv6 BGP Table Size predictions
Jan 2013 11,600 entries
2014 16,200
2015 21,000
2016 30,000 25,000
2017 42,000 29,000
2018 58,000 34,000
2019 82,000 38,000
2019 113,000 43,000
Exponential Model
Linear Model
Range of potential outcomes

## Slide 36: BGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing at a faster relative rate, is still small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet
Nothing is melting in terms of the size of the routing table as yet

## Slide 37: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 38: Announcements and Withdrawals

## Slide 39: Convergence Performance

## Slide 40: IPv4 Average AS Path Length
Data from Route Views

## Slide 41: Updates in IPv4 BGP
Nothing in these figures is cause for any great level of concern …
  The number of updates per instability event has been constant, which for a distance vector routing protocol is weird, and completely unanticipated. Distance Vector routing protocols should get noisier as the population of protocol speakers increases, and the increase should be multiplicative.
  But this is not happening in the Internet
  Which is good, but why is this not happening?
  Likely contributors to this +ve outcome are the damping effect of widespread use of the MRAI interval, and the topology factor, as seen in the relatively constant AS Path length over this interval

## Slide 42: V6 Announcements and Withdrawals

## Slide 43: V6 Convergence Performance

## Slide 44: V6 Average AS Path Length
Data from Route Views

## Slide 45: Updates in IPv6 BGP
IPv6 updates look a lot like IPv4 updates.
  Which should not come as a surprise
  It’s the same routing protocol, and the same underlying inter-AS topology, and the observation is that the convergence times and instability rate appear to be unrelated to the population of the routing space.
So we see similar protocol convergence metrics in a network that is 1/20 of the size of the IPv4 network
It tends to underline the importance of dense connectivity and extensive use of local exchanges to minimize AS path lengths as a means of containing scaling of the routing protocol

## Slide 46: Problem? Not a Problem?
There is nothing is this data to suggest that we will need a new inter-domain routing protocol in the next 5 years
Or even in the next 10 to 15 years
But this is not the only scaling aspect of the Internet
Remember that BGP is a Best Path selection protocol. i.e. a single path selection protocol.
And that might contribute to the next scaling issue…

## Slide 47: Inside a router
Backplane
Line Interface Card
Switch Fabric Card
Management Card
Thanks to Greg Hankins

## Slide 48: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 49: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 50: FIB Lookup Memory
The interface card’s network processor passes the packet’s destination address to the FIB module.
The FIB module returns with an outbound interface index

## Slide 51: FIB Lookup
This can be achieved by:
  Loading the entire routing table into a Ternary Content Addressable Memory bank (TCAM)
or
  Using an ASIC implementation of a TRIE representation of the routing table with DRAM memory to hold the routing table
Either way, this needs fast memory

## Slide 52: TCAM Memory
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
192.0.0.0/16 11000000 00000000 xxxxxxxx xxxxxxxx 3/0
192.0.2.0/24 11000000 00000000 00000010 xxxxxxxx 3/1
11000000 00000000 00000010 00000001
Longest Match
The entire FIB is loaded into TCAM. Every destination address is passed through the TCAM, and within one TCAM cycle the TCAM returns the interface index of the longest match. Each TCAM bank needs to be large enough to hold the entire FIB. TTCAM cycle time needs to be fast enough to support the max packet rate of the line card.
TCAM width depends on the chip set in use. One popular TCAM config is 72 bits wide. IPv4 addresses consume a single 72 bit slot, IPv6 consumes two 72 bit slots. If instead you use TCAM with a slot width of 32 bits then IPv6 entries consume 4 times the equivalent slot count of IPv4 entries.

## Slide 53: TRIE Lookup
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
11000000 00000000 00000010 00000001
1/0
1/0
1/0
1/0
1/0
x/0000
?
?
?
?
?
…
?
The entire FIB is converted into a serial decision tree. The size of decision tree depends on the distribution of prefix values in the FIB. The performance of the TRIE depends on the algorithm used in the ASIC and the number of serial decisions used to reach a decision
ASIC
DRAM

## Slide 54: Memory Tradeoffs
TCAM
Lower
Higher
Higher
Higher
Larger
80Mbit
ASIC +
RLDRAM 3
Higher
Lower
Lower
Lower
Smaller
1Gbit
Thanks to Greg Hankins
Access Speed
$ per bit
Power
Density
Physical Size
Capacity

## Slide 55: Memory Tradeoffs
TCAMs are higher cost, but operate with a fixed search latency and a fixed add/delete time. TCAMs scale linearly with the size of the FIB
ASICs implement a TRIE in memory. The cost is lower, but the search and add/delete times are variable. The performance of the lookup depends on the chosen algorithm. The memory efficiency of the TRIE depends on the prefix distribution and the particular algorithm used to manage the data structure

## Slide 56: Size
What memory size do we need for 10 years of FIB growth from today?
TCAM
V4: 2M entries (1Gt)
plus
V6: 1M entries (2Gt)
2014
2019
2024
512K
25K
125K
1M
768K
512K
V6 FIB
V4 FIB
Trie
V4: 100Mbit memory (500Mt)
plus
V6: 200Mbit memory (1Gt)
“The Impact of Address Allocation and Routing on the Structure and
Implementation of Routing Tables”, Narayn, Govindan & Varghese, SIGCOMM ‘03

## Slide 57: Scaling the FIB
BGP table growth is slow enough that we can continue to use simple FIB lookup in linecards without straining the state of the art in memory capacity
However, if it all turns horrible, there are alternatives to using a complete FIB in memory, which are at the moment variously robust and variously viable:
  FIB compression
  MPLS
  Locator/ID Separation (LISP)
  OpenFlow/Software Defined Networking (SDN)

## Slide 58: But it’s not just size
It’s speed as well.
10Mb Ethernet had a 64 byte min packet size, plus preamble plus inter-packet spacing
=14,880 pps
=1 packet every 67usec
We’ve increased speed of circuits, but left the Ethernet framing and packet size limits largely unaltered. What does this imply for router memory?

## Slide 59: Wireline Speed – Ethernet
1980
1990
2000
2010
2020
1Tb
10Mb
100Mb
1Gb
10Gb
100Gb
10Mb 1982/15Kpps
100Mb 1995 / 150Kpps
1Gb 1999 / 1.5Mpps
10Gb 2002 / 15Mpps
40Gb/100Gb 2010 / 150Mpps
400Gb/1Tb 2017?
1.5Gpps

## Slide 60: Clock Speed – Processors
1980
1990
2000
2010
2020
100Ghz
1Mhz
10Mhz
100Mhz
1GHz
10GHz
8080 2Mhz 1981
Dec Alpha 100Mz 1992
AMD 1GHz 2000
P4 3Ghz 2002
zEC12 5.5Ghz 2012

## Slide 61: Clock Speed – Processors

## Slide 62: CPU vs Memory Speed

## Slide 63: Speed, Speed, Speed
What memory speeds are necessary to sustain a maximal packet rate?
100GE 150Mpps 6.7ns per packet
400Ge 600Mpps 1.6ns per packet
1Te 1.5Gpps 0.67ns per packet
0ns
10ns
20ns
30ns
40ns
50ns
100Ge
400Ge
1Te

## Slide 64: Speed, Speed, Speed
What memory speeds do we have today?
0ns
10ns
20ns
30ns
40ns
50ns
Commodity DRAM
DDR3DRAM= 9ns -15ns
RLDRAM = 1.9ns - 12ns
Thanks to Greg Hankins
100Ge = 6.7ns
400Ge =1.67ns
1Te = 0.67ns

## Slide 65: Scaling Speed
Scaling size is not a dramatic problem for the Internet of today or even tomorrow
Scaling speed is going to be tougher over time
Moore’s Law talks about the number of gates per circuit, but not circuit clocking speeds
Speed and capacity could be the major design challenge for network equipment in the coming years
http://www.startupinnovation.org/research/moores-law/

## Slide 66: Scaling Speed
If we can’t route the max packet rate for a Terrabit wire then:
Should the IEEE standards group recognise this and support a case to reduce the max packet rate by moving away from a 64byte min packet size for the 1Tb 802.3 standard?
Can we push this into Layer 3? if we want to exploit parallelism as an alternative to wireline speed for terrabit networks, then is the use of best path routing protocols, coupled with destination-based hop-based forwarding going to scale?
Or do we start to tinker with the IP architecture itself? Are we going to need to look at path-pinned routing architectures to provide stable flow-level parallelism within the network to limit aggregate flow volumes?
http://www.startupinnovation.org/research/moores-law/

## Slide 67
Thank You
Questions?