## Slide 1: Measuring ATR
Joao Damas
Geoff Huston
@apnic.net
May 2018

## Slide 2: September 2017:

## Slide 3: The Internet has a problem …
Instead of evolving to be more flexible and more capable, it appears that the Internet’s transport is becoming more ossified and more inflexible in certain aspects
One of the major issues here is the handling of large IP packets and IP level packet fragmentation
We are seeing a number of end-to-end paths on the network that no longer support the carriage of fragmented IP datagrams
We are concerned that this number might be getting larger, not smaller

## Slide 4: The Internet has a problem …
What about the DNS?
  One application that is making increasing use of large UDP packets is the DNS
  This is generally associated with DNSSEC-signed responses (such as “dig +dnssec DNSKEY org”) but large DNS responses can be generated in other ways as well (such as “dig . ANY”)
  In the DNS we appear to be relying on the successful transmission of fragmented UDP packets, but at the same time we see an increasing problem with the coherence in network and host handling of fragmented IP packets, particularly in IPv6

## Slide 5: Changing the DNS?
But don’t large DNS transactions use TCP anyway?
  In the original DNS specification only small (smaller than 512 octets) responses are passed across UDP.
  Larger DNS responses are truncated and the truncation is intended to trigger the client to re-query using TCP
  EDNS(0) allowed a client to signal a larger truncation size threshold, and assumes that fragmented DNS is mostly reliable
  But what if it’s not that reliable?

## Slide 6: What is “ATR”?
It stands for “Additional Truncated Response”
  Internet draft: draft-song-atr-large-resp-01
    May 2018
    Linjian (Davey) Song, Beijing Internet Institute
It’s a hybrid response to noted problems in IPv4 and IPv6 over handling of large UDP packets and IP fragmentation
ATR adds an additional response packet to ‘trail’ a fragmented UDP response
The additional response is just the original query with the Truncated bit set, and the sender delays this additional response packet by 10ms

## Slide 7: The Intention of ATR
Today:
If the client cannot receive large truncated responses then it will need to timeout from the original query,
Then re-query using more resolvers,
Timeout on these queries
Then re-query using a 512 octet EDNS(0) UDP buffersize
Then get a truncated response
Then re-query using TCP

## Slide 8: The Intention of ATR
Today:
If the client cannot receive large truncated responses then it will need to timeout from the original query,
Then re-query using more resolvers,
Timeout on these queries
Then requery using a 512 octet EDNS(0) UDP buffersize
Then get a truncated response
Then requery using TCP
within a few ms
ATR

## Slide 9: The Intention of ATR
When a UDP DNS response is fragmented by the server, then the server will also send a delayed truncated UDP DNS response
  The delay is proposed to be 10ms
If the DNS client receives and reassembles the fragmented UDP response the ensuing truncated response will be ignored
If the fragmented response is lost due to fragmentation loss, then the client will receive the short truncated response
The truncation setting is intended to trigger the client to re-query using TCP without further delay

## Slide 10: ATR Operation
UDP DNS Query
Client
Server

## Slide 11: ATR Operation
UDP DNS Query
UDP DNS Response
(Fragmented)
Client
Server

## Slide 12: ATR Operation
UDP DNS Query
UDP DNS Response
(Fragmented)
UDP DNS Response
(Truncated)
10ms
Client
Server

## Slide 13: ATR Operation
UDP DNS Query
UDP DNS Response
(Fragmented)
UDP DNS Response
(Truncated)
10ms
Client
Server
TCP Query and Response

## Slide 14: What could possibly go wrong?
Network level packet re-ordering may cause the shorter truncated response packet to overtake the fragmented response, causing an inflated TCP load, and the potential for TCP loss to be triggered
Not every client DNS system supports using TCP to emit queries

## Slide 15: ATR and Resolver Behaviour
Can’t Receive Fragmented UDP
Can’t Use TCP
ATR will help
ATR won’t be of use, but it
shouldn’t matter
ATR won’t help

## Slide 16: ATR and Resolver Behaviour
Can’t Receive Fragmented UDP
Can’t Use TCP
How big are each of these pools?
What proportion of users are impacted?
ATR will help
ATR won’t be of use, but it
shouldn’t matter
ATR won’t help

## Slide 17: Experiment Details
Use 6 tests:
  2 tests use ATR responses – one is DNS over IPv4, the other is DNS over IPv6
  2 tests use only truncated responses – IPv4 and IPv6
  2 tests use large fragmented UDP responses - IPv4 and IPv6
Performed 55M experiments

## Slide 18: Looking at Resolvers
We are looking at resolvers who demonstrated that they received responses of each test type:
Protocol | Resolvers | ATR | Large UDP | TCP
IPv4 | 113,087 | 71.2% | 60.1% | 79.4%
IPv6 | 20,878 | 55.4% | 50.0% | 55.1%

## Slide 19: Looking at Resolvers
We are looking at resolvers who demonstrated that they received responses of each test type:
Protocol | Resolvers | Fail ATR | Fail Large UDP | Fail TCP
IPv4 | 113,087 | 28.8% | 39.9% | 20.6%
IPv6 | 20,878 | 44.6% | 50.0% | 44.9%
Inversely, lets report on the FAILURE rate of resolvers

## Slide 20: Seriously?
More than one third of the ”visible” IPv4 resolvers are incapable of receiving a large fragmented packet
And one half of the ”visible” IPv6 resolvers are incapable of receiving a large fragmented packet

## Slide 21: ASNs of IPv4 Resolvers that do not followup when given a large UDP Response – Top 10
ASN | Use | Exp | AS Name | CC
AS9644 | 0.78% | 447,019 | SK Telecom | KR
AS701 | 0.70% | 400,798 | UUNET - MCI Communications Services | US
AS17853 | 0.62% | 357,335 | LGTELECOM | KR
AS4766 | 0.59% | 340,334 | Korea Telecom | KR
AS4134 | 0.47% | 267,995 | CHINANET-BACKBONE | CN
AS31034 | 0.47% | 267,478 | ARUBA-ASN | IT
AS3786 | 0.39% | 225,296 | DACOM Corporation | KR
AS36692 | 0.38% | 217,306 | OPENDNS - OpenDNS | US
AS3215 | 0.33% | 189,810 | Orange | FR
AS812 | 0.30% | 169,699 | ROGERS COMMUNICATIONS | CA

## Slide 22: ASNs of IPv6 Resolvers that do not followup when given a large UDP Response – Top 10
ASN | Use | Exp | AS Name | CC
AS15169 | 40.60% | 10,006,596 | Google | US
AS5650 | 0.90% | 221,493 | Frontier Communications | US
AS36692 | 0.84% | 206,143 | OpenDNS | US
AS812 | 0.78% | 193,073 | Rogers Communications Canada | CA
AS20057 | 0.46% | 114,440 | AT&T Mobility LLC | US
AS3352 | 0.38% | 92,925 | TELEFONICA_DE_ESPANA | ES
AS852 | 0.35% | 85,043 | TELUS Communications Inc. | CA
AS55644 | 0.32% | 80,032 | Idea Cellular Limited | IN
AS3320 | 0.25% | 61,938 | DTAG Internet service provider operations | DE
AS4761 | 0.24% | 60,019 | INDOSAT-INP-AP INDOSAT Internet Network Provider | ID

## Slide 23: ASNs of IPv4 Resolvers that do not followup in TCP when given a truncated UDP Response – Top 10
ASN | Use | Exp | AS Name | CC
AS9299 | 0.55% | 252,653 | Philippine Long Distance Telephone | PH
AS24560 | 0.34% | 155,908 | Bharti Airtel | IN
AS3352 | 0.29% | 132,924 | TELEFONICA_DE_ESPANA | ES
AS9498 | 0.19% | 84,754 | BHARTI Airtel | IN
AS9121 | 0.14% | 61,879 | TTNET | TR
AS23944 | 0.13% | 58,102 | SKYBroadband | PH
AS9644 | 0.11% | 51,750 | SK Telecom | KR
AS24499 | 0.11% | 51,108 | Telenor Pakistan | PK
AS3215 | 0.10% | 43,614 | Orange | FR
AS23700 | 0.09% | 39,697 | Fastnet | ID

## Slide 24: ASNs of IPv6 Resolvers that do not followup in TCP when given a truncated UDP Response – Top 10
ASN | Use | Exp | AS Name | CC | 
AS15169 | 4.15% | 961,287 | Google | US | 
AS21928 | 1.72% | 399,129 | T-Mobile USA | US | 
AS7922 | 1.57% | 364,596 | Comcast Cable | US | 
AS3352 | 0.54% | 126,146 | TELEFONICA_DE_ESPANA | ES | 
AS22773 | 0.38% | 87,723 | Cox Communications Inc. | US | 
AS55644 | 0.35% | 80,844 | Idea Cellular Limited | IN | 
AS20115 | 0.31% | 71,831 | Charter Communications | US | 
AS20057 | 0.30% | 70,518 | AT&T Mobility | US | 
AS6713 | 0.20% | 46,196 | IAM-AS | MA | 
AS8151 | 0.20% | 45,754 | Uninet S.A. de C.V. | MX | 

## Slide 25: What’s the impact?
Counting resolvers is NOT the same as counting users!
Failure in the DNS is often masked by having multiple resolvers in the clients local configuration
And the distribution of users to visible recursive resolvers is heavily skewed (10,000 resolvers by IP address handle the DNS queries of some 90% of all end users)
To assess the user impact let’s look at the results by counting user level success / failure

## Slide 26: Looking at Users - Failure Probabilities
IPv4
UDP Frag: 12.5%
TCP: 4.0%
ATR 3.9%
IPv6
UDP Frag: 20.8%
TCP: 8.4%
ATR 6.5%

## Slide 27: ATR and Resolver Behaviour – IPv4
Can’t Receive Fragmented UDP
Can’t Use TCP
ATR will help
ATR won’t be of use, but it
shouldn’t matter
ATR won’t help
12.5%
4.0%
8.6% 3.9% 0.1%

## Slide 28: ATR and Resolver Behaviour – IPv4 IPv6
Can’t Receive Fragmented UDP
Can’t Use TCP
ATR will help
ATR won’t be of use, but it
shouldn’t matter
ATR won’t help
12.5%
4.0%
20.8%
14.3% 6.5% 1.9%
8.4%
8.6% 3.9% 0.1%

## Slide 29: ATR Impact: Net Change in User Failure Rates
IPv4
Fragged UDP Loss: 12.5%
ATR Loss Rate: 3.9%
IPv6
Fragged UDP Loss: 20.8%
ATR Loss Rate: 6.5%

## Slide 30: Why use ATR?
Allows those resolvers that can receive large fragmented UDP packets to do so without being pushed into using TCP
  In this case the trailing truncated packet is ignored
    (or, at worst, generates an ICMP Port Unreachable message back to the server)
Faster resolution when fragmented UDP responses are blocked
  The ATR switchover to TCP happens immediately rather than waiting for local timeouts to perform EDNS(0) UDP Buffer Size hunting to trigger a truncated response
    Less time to resolve, fewer packets to resolve

## Slide 31: Why NOT use ATR?
Large UDP responses are used in DDOS attacks - adding an additional packet to the response adds to the DDOS amplification factor
The trailing UDP packet may generate ICMP Port Unreachable messages back to the server
  (This IMCP message occurs about at a rate of approximately 1 in 5 responses in our experiments)
Potential DDOS vector for the server
  (unless the server limits the queue of delayed packets to some arbitrary ceiling)
Potential re-ordering of the responses in flight may cause an unnecessary delay and an additional TCP local component
  (This can be reduced by using a longer delay, but too long a delay will allow for clients to requery)
One more straw to add to the back of the DNS camel!

## Slide 32: ATR Assessment
Is this level of benefit worth the additional server and traffic load when sending large responses?
  Is this load smaller than resolver hunting in response to packet drop?
  Is the faster fallback to TCP for large responses a significant benefit?
Do we have any better ideas about how to cope with large responses in the DNS?

## Slide 33: Thanks!